## Slide 1
ACADEMIC PROJECT PRESENTATION • PACELINK
Energy Depletion Attacks
on Cardiac Pacemakers
A server-mediated isolation architecture that keeps the implant
unreachable by anything except a brief, scheduled sync.
Hospital App • Patient Mobile App • Isolated Pacemaker Link
Notes: Title slide. Introduce the project as a security-focused implementation: a hospital + patient app system whose core contribution is isolating the implanted pacemaker from direct network exposure to defend against energy depletion attacks.

## Slide 2
OVERVIEW
What We'll Cover
01
The Threat
What an energy depletion attack is, and why implants are uniquely exposed to it.
02
Attack Mechanics
How an attacker forces a pacemaker's radio and pacing circuitry to burn through a fixed battery budget.
03
Our System
A hospital app and patient mobile app that never let the implant be directly reachable.
04
Architecture & Defense
How the design maps directly onto each attack vector, and what's left to harden.
02
Notes: Four-part agenda. Keep this brief — under a minute — and reference it verbally when transitioning between the threat-model half and the system half of the talk.

## Slide 3
THE THREAT
What Is an Energy Depletion Attack?
A denial-of-service attack aimed at a device's power budget, not its logic. Instead of crashing or corrupting a battery-powered device, the attacker repeatedly forces it to perform its most power-hungry operations — radio transmission, cryptographic handshakes, actuation — far more often than the device's normal workload requires.
First formalized for implantable medical devices in the IMD security literature (e.g. Halperin et al., 2008), which showed that a pacemaker/ICD's wireless telemetry interface could be abused to drain a battery meant to last years, not sessions.
Why implants are a special case
Sealed, non-rechargeable battery — depletion means surgery, not a charger.
Typical implant life: 5–15 years by design — an attacker only needs to shorten that.
The economics of the attack
ATTACKER COST
Low
no need to break crypto or pacing logic — just keep the radio busy
DETECTABILITY
Low
looks like ordinary telemetry traffic, not a crash or an error
PATIENT IMPACT
Delayed but severe
premature replacement surgery, or therapy denied once depleted
03
Notes: Define the attack class in general terms before narrowing to pacemakers specifically. The Halperin et al. 2008 citation gives this academic grounding without needing to fabricate statistics.

## Slide 4
THE THREAT
How the Attack Targets a Pacemaker
Repeated interrogation
Flooding the telemetry radio with read/status requests, forcing it to wake and answer far more often than a clinic visit ever would.
Forced extra pacing
Issuing spoofed or excessive pacing/voltage commands — every extra pulse burns real energy from a fixed budget.
Extended listening windows
Keeping a session or advertising window open longer than needed, so the radio idles in an expensive active state.
The result isn't a crash — it's a shortened life
Premature battery depletion → early, avoidable replacement surgery
Unpredictable failure timing → clinicians lose the years-long planning window
Therapy denied → once depleted, the device can no longer pace at all
04
Notes: Three attack mechanics, then a consequences strip. Emphasize that the attacker never needs to defeat the pacing algorithm or any cryptography — simply keeping the radio busy is enough.

## Slide 5
PROBLEM STATEMENT
Why a Directly-Reachable Implant Is the Vulnerability
In a naive design, the implant's radio is reachable at any time by whatever can reach its link — a hospital server, an app, or an attacker who spoofs either. That link is the entire attack surface an energy depletion attack needs.
Attacker
spoofs or floods the link
always-open / always-reachable link
Pacemaker
radio wakes for every request
No isolation boundary means no limit on how often, or by whom, the implant's radio can be triggered.
05
Notes: This is the problem statement slide: name the vulnerability precisely as 'no isolation boundary between the implant and anything that can reach its link', which sets up the next slide's thesis directly.

## Slide 6
OUR APPROACH
Isolate the Pacemaker, Not Just Secure It
Our system never lets the implant be directly reachable by the hospital server, the internet, or an app running on someone else's phone. The only party that can ever reach it is the patient's own paired phone — and only for a fraction of a second, on a schedule.
BEFORE — Direct Link
Implant radio reachable continuously
Anything that reaches the link can trigger it
No cap on request frequency
Attack window: effectively unlimited
AFTER — Isolated Relay
Implant radio idle/advertising-only by default
Only the one paired phone can ever open a session
Session self-closes in well under 1s, hard-capped at 5s
Attack window: ~1s every 30 minutes
06
Notes: The thesis slide. 'Isolate' is the operative word: we are not primarily relying on encryption or authentication at the implant — we are minimizing the time window during which the implant is reachable at all.

## Slide 7
SYSTEM DESIGN
System Architecture
Hospital Web App
doctor: register, prescribe voltage, view readings
Django Server
token auth • queued voltage • heart-rate store
Patient Mobile App
Expo / React Native • 30-min sync cycle
transient link
Pacemaker
isolated — reachable only mid-session
Tech Stack
Backend
Django, token auth, hand-rolled CORS, SQLite
Patient App
Expo SDK 51, React Native 0.74, expo-router
Device Link
PacemakerLink abstraction — BLE / HTTP-sim / mocked, one interface
AI Assistant
Gemini-backed Heart Assistant for patient education
07
Notes: Walk left to right: hospital app queues a prescribed voltage on the server; the phone is the only thing that ever bridges the server and the implant, and only briefly. The tech-stack strip below grounds the diagram in what was actually built.

## Slide 8
HOSPITAL SIDE
Doctor Portal Workflow
01
Register the patient
Doctor creates a patient record; a login is provisioned for their mobile app under the doctor's own account scope.
02
Prescribe a voltage
Doctor sets a target voltage, bounded server-side to a safe 0.5V–7.5V range (default 2.5V) — never applied directly to the device.
03
Change is queued
The prescription is stored as a pending VoltageChange, marked unpushed until the patient's phone actually delivers it.
04
Monitor readings
Heart-rate history the phone has synced back is available on the dashboard for review between visits.
08
Notes: Emphasize the queue: a doctor's prescription does not go straight to the implant. It waits as a pending VoltageChange until the patient's own phone is the one to deliver it during a sync.

## Slide 9
PATIENT SIDE
Patient Mobile App: The Sync Cycle
Every 30 minutes — or on demand, when the patient taps “Sync now” — the app runs one short, self-contained cycle:
Connect
Phone opens a session with the implant; it wakes and hands back a one-time session id.
Write
Phone writes the doctor-prescribed voltage it last pulled from the server.
Read
Phone reads back whatever heart-rate data the implant has collected since the last visit.
Disconnect
Session closes explicitly; the implant returns to idle/advertising-only — isolated again.
< 1 second typical connect→disconnect duration, shown live on the dashboard (e.g. “connected 41ms then isolated”) • 5s hard cap — the server force-closes any session that outlives it, even after a client crash.
09
Notes: This is the mechanical core of the defense. Point out PacemakerLink as an abstraction: the same four calls (connect/writeVoltage/readHeartRates/disconnect) are implemented three ways — network (HTTP demo), ble (react-native-ble-plx, real GATT), and simulated — so swapping to real hardware is a one-line config change, not a rewrite.

## Slide 10
DEFENSE RATIONALE
Mapping the Defense to Each Attack Vector
Repeated interrogation
Radio is idle/advertising-only except a ~1s window every 30 min — there's almost nothing to interrogate.
Forced extra pacing
Only a server-vetted, doctor-issued, 0.5–7.5V-bounded instruction is ever relayed — no external party can inject one.
Extended listening windows
Sessions self-close in milliseconds; a 5s hard timeout force-closes stragglers; every response sends Connection: close.
10
Notes: This slide directly answers 'so what' — each row pairs an attack mechanic from slide 4 with the specific mechanism (from slide 9) that closes it. This is the strongest evaluative slide in the deck; spend real time here.

## Slide 11
DEFENSE IN DEPTH
Safeguards Beyond Isolation
Token authentication
Every hospital-app ↔ server and phone ↔ server call requires a bearer token; no session cookies to hijack.
Server-enforced voltage bounds
0.5V–7.5V is enforced in the data model itself, not just the UI — a compromised client still can't request an unsafe value.
Acknowledged, not blind-pushed
A voltage change is marked pushed only after the phone confirms what it actually wrote — no fire-and-forget commands to the implant.
Self-expiring sessions
A 5-second server-side timeout closes any session the client doesn't, even after a crash — isolation never depends on the client behaving.
11
Notes: These are supporting safeguards, not the headline defense — make clear isolation (previous slides) is the primary mitigation, and this slide is what protects the parts of the system that remain online (server, apps).

## Slide 12
HONEST ASSESSMENT
Challenges & Limitations
No physical BLE hardware yet
The demoed link uses an HTTP-based simulator standing in for real GATT; behavior is modeled, not measured on radio hardware.
Phone is a single point of trust
If the paired phone itself is compromised, it's still the one party allowed to reach the implant.
OS background scheduling
Mobile OS power management can delay the 30-minute background sync; on-demand sync is the fallback, not a guarantee.
Doesn't address physical-layer jamming
Isolation defeats protocol-level flooding, not RF jamming that doesn't rely on a valid session at all.
12
Notes: An evaluator will ask about at least one of these unprompted — naming them first shows the isolation model is understood as a mitigation, not a silver bullet.

## Slide 13
WHAT'S NEXT
Future Scope
01
Real BLE hardware
Swap in the existing BlePacemaker implementation against an ESP32 flashed as a GATT peripheral — no app-layer changes needed.
02
Measure the attack window
Instrument real radio timing to quantify the reduction in exposure versus a naive always-on link.
03
Signed voltage instructions
Add a signature the phone can verify before writing, so a compromised server can't silently push an unsafe value.
04
Anomaly detection on sync cadence
Flag sync attempts that deviate from the 30-minute pattern as a possible depletion attempt in progress.
13
Notes: Order roughly by how directly each extends the current isolation architecture versus adding a new layer on top of it.

## Slide 14
Thank You
Questions on the isolation architecture, the sync protocol, or the threat model are welcome.
PaceLink • Energy Depletion Attack Defense
Notes: Closing slide. Invite questions specifically about the sync protocol timing and the threat model — those are the two areas most likely to get probing follow-ups.